This completed form, and associated rack weight and balance information, is due to the AIC by Monday, November 17, 2015 for the SONGNEX project.

I.  General information:

1.  Mission name:  SONGNEX 2015

2.  Instrument name: 	SO2, CO

3.  What is measured: 	SO2, CO

4.  Short description of measurement technique:

SO2:	Pulsed UV Fluorescence

CO:	Resonant VUV Fluorescence

5. Contact information for all personnel going to the field with this instrument:

(for multiple investigators, please list the PI or primary contact person first)

| Name | Email | Office phone | Cell phone |
| --- | --- | --- | --- |
| 1. John Holloway | john.s.holloway@noaa.gov | (303) 497-3273 |  |
| 2. |  |  |  |
| 3. |  |  |  |
| 4. |  |  |  |
| 5. |  |  |  |
| 6. |  |  |  |

I.  Specific information:

1. Total installed weight:	237.5 lbs

(rack, gas cylinders, hoses, cabling, pumps, inlets, permeation tubes, etc.)

| Rack weight and balance info | Allowed | Actual |
| --- | --- | --- |
| Weight, lbs.: | 263 lbs | 237.5 lbs |
| Overturning moment, in-lbs.: | 7875 in-lbs | 5489 in-lbs |

Pod weight and CG: 	CO: 350 lbs / within ±3.0 in. of center of mounting lugs as per MIL-STD-8591, 5.7.1.2

NOTE: Please also provide weight-and-balance information for all installed equipment.  Templates for standard electronics racks are available for download here.  PIs with non-standard installations will need to provide relevant information in a similar format.

2.  Individual subassembly info (weights should sum to total listed above)

| Component name | Location name and flight station | Weight, lbs |
| --- | --- | --- |
| 1.gas bottle tray | Station 6 / F.S 788 | 54 |
| 2.computer | Station 6 / F.S 788 | 28 |
| 3.data system | Station 6 / F.S 788 | 13 |
| 4.TECO SO2 intr. | Station 6 / F.S 788 | 55 |
| 5.kbd./monitor tray | Station 6 / F.S 788 | 20 |
| 6.sample pump | Station 6 / F.S 788 | 19 |
| 7.power distribution panel | Station 6 / F.S 788 | 3.5 |
| 8.instrument rack w/ floor plates | Station 6 / F.S 788 | 38 |
| 9. cabling and tubing | Station 6 / F.S 788 | 7 |

3.  Component power consumption in Amps

| Component name | Location name | 400 Hz 3Ø | 400 Hz 1Ø | 60 Hz | 28VDC | 28VDC WOW |
| --- | --- | --- | --- | --- | --- | --- |
| 1.SO2 instrumentation | Sta. 6 |  | 3(6) A |  |  | 0.1 A |
| 2.CO wing pod | R.W.S. 465 |  | 6(10) A |  |  |  |
| 3. |  |  |  |  |  |  |
| 4. |  |  |  |  |  |  |
| 5. |  |  |  |  |  |  |
| 6. |  |  |  |  |  |  |
| 7. |  |  |  |  |  |  |
| 8. |  |  |  |  |  |  |
| 9. |  |  |  |  |  |  |
| 10. |  |  |  |  |  |  |
| 11. |  |  |  |  |  |  |
| 12. |  |  |  |  |  |  |
|  | Totals: |  | 9 A |  |  | 0.1 A |
|  |  | 400 Hz 3Ø | 400 Hz 1Ø | 60 Hz | 28VDC | 28VDC WOW |

4.  Inlet and exhaust information:

| Inlet/exhaust name | Location name and flight station | Hole size through hull, inches |
| --- | --- | --- |
| 1. SO2 inlet | Sta. 5 window / F.S. 764 | 3.7 in. (existing window plate) |
| 2. SO2 exhaust | LIPF venturi plate, F.S. 780 | 3/8 tubing venting through rearward rakes on venturi plate |
| 3. |  |  |
| 4. |  |  |
| 5. |  |  |
| 6. |  |  |

5.  Source of flow (name and location of pump or venturi)

| Pump name | Location name and flight station |
| --- | --- |
| 1. SO2 diaphragm pump | Sta. 6 /F.S. 788 |
| 2. CO diaphragm pump | CO wing pod / R.W.S 465 |
| 3. |  |
| 4. |  |
| 5. |  |
| 6. |  |

6.  Installed hazardous materials or equipment:

(only for items installed in the aircraft for use during flight)

A.  Lasers	n/a

B.  RF transmitters:	n/a

C.  Radioactive materials:	n/a

D.  Compressed gases: (1 ft3 = 28.32 liters; cabin volume = 4260 ft3 = 1.21 x 105 liters)

| Cylinder number: | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| Gas description | SO2/N2 | pure air | CO2/Ar | CO/air | pure air |
| Mixing ratio | 10 ppmv |  | 0.25% | 10 ppmv |  |
| Cylinder size (ft3) | 30 | 30 | 10 | 10 | 10 |
| Max pressure (psig) | 1800 | 2000 | 1500 | 1500 | 1500 |
| # installed on aircraft | 1 | 1 | 1 | 1 | 1 |
| Location on aircraft | Sta. 6 | Sta. 6 | R.W.S. 465 | R.W.S. 465 | R.W.S. 465 |
| Service frequency | none | every 5 flights | every 6 flights | none | every 10 flights |
| toxic/flammable gases: |  |  |  |  |  |
| In containment vessel? |  |  |  |  |  |
| Gas alarm provided? |  |  |  |  |  |
| MR if vented to cabin, ppmv |  |  |  |  |  |
| OSHA 8-hr PEL, ppmv |  |  |  |  |  |
| 30-min IDLH, ppmv |  |  |  |  |  |

E.  Chemicals (solids and liquids):

| Chemical number: | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Concentration |  |  |  |  |  |  |
| Amount |  |  |  |  |  |  |
| Container description |  |  |  |  |  |  |
| Purpose |  |  |  |  |  |  |
| Solution pH |  |  |  |  |  |  |
| Spill kit provided? |  |  |  |  |  |  |

F.  Cryogens:  n/a

G.  UPS and battery installation:  n/a

H.  Motors

Description: SO2 diaphragm pump

Motor current draw 1Ø, 400Hz, 1.5 A / 0.6 A

(e.g., 3Ø, 400Hz, 8A startup, 4A running)

Thermal interlock enabled? yes

Description: CO diaphragm pump

Motor current draw 1Ø, 400Hz, 2.4 A / 1.0 A

(e.g., 3Ø, 400Hz, 8A startup, 4A running)

Thermal interlock enabled? yes

Operator seat requests -

Test flights: 1 seat for 1 flight

Transit flights:	 1 seat

Science flights: 1 seat

7.  Data and plumbing drops

Network (Cat. 5/6 ethernet) drops requested: F.S 788 and R.W.S. 465

Serial drops requested: F.S. 788

IRIG-B drops (BNC coax connector) requested: F.S. 788 (in absence of network time server)

Vacuum/exhaust/ emergency dump lines:

| Name | Flow rate, slpm | Line pressure, Torr | Pump type | Trace gas concentration(s) |
| --- | --- | --- | --- | --- |
| 1. SO2 diaphragm pump | 5 std-l/min | atmospheric | diaphragm | 10 ppbv SO2 |
| 2. |  |  |  |  |
| 3. |  |  |  |  |
| 4. |  |  |  |  |

Ground gas service lines (number, location, type of service):

one ¼” line from Sta. 6 to freefall chute for pure air (run in pre-flight)

Other gas lines (number, location, type of service):

Will you be sending data to the AOC data station?  If so, please provide the following information:

| Parameter name | Voltage range | Unit conversion |
| --- | --- | --- |
| 1. |  |  |
| 2. |  |  |
| 3. |  |  |

8.  Aircraft access

a.  flight days:

Pre-flight time requested at aircraft (hours):	1.5 hr.

Routine pre-flight ground support required?

(stands, ladders, forklifts, covers, external equipment, etc.)

cover removal; ladder at Sta. 5 window

occasional stand; R.W.S. 465 pod

Routine post-flight time requested at aircraft (hours): 1.0 hr.

Routine post-flight ground support required?

(stands, ladders, forklifts, covers, external equipment, etc.)

cover replacement; ladder at Sta. 5 window

stand; R.W.S. 465 pod

b.  non-flight days:

Routine external access to inlets or zenith mounts required?

(please describe location, how often, for how long, type of ground support equipment needed, weather constraints, etc.)

stand to RWS 465 for compressed gas refill, every 50 flight hours

Please note there is zero access and zero power to the aircraft (including pods) on hard-down days.  These occur at least once every seven calendar days while in the field.

9.  Aircraft maneuvers

Briefly describe in-flight calibration frequency, duration, altitudes desired:

SO2: periodic in-situ calibration consisting of 60 s instrument zero on 20 min period; 60 s sensitivity by std. addition on 40 min period.  All altitudes necessary to determine pressure dependence.

CO: periodic in-flight calibration consisting of 40 second instrument zero 			on 15 minute period; 40 second sensitivity by std. addition on 30 minute 			period.

Briefly describe instrument sensitivity to flight conditions:

(issues during roll/pitch, ascent/descent, sampling in cloud, icing etc.)

SO2: potential of aspirating liquid water in clouds

10.  Miscellaneous

1.  Hazmat for preflight/postflight calibrations:  Please describe fully any additional hazardous materials - compressed gases, solvents, radioactive ion sources – that you anticipate temporarily bringing onto the aircraft for periodic instrument calibration purposes  (e.g., n-butanol in a CN counter, 210Po in a DMA, a UPS for power, compressed gas cylinders for calibrations, etc.)

Compressed N2 gas to R.W.S. 465 pod postflight.

2.  Fabrication and sheet metal support:  Please describe fully any anticipated requests for fabrication or sheet-metal support during installation in Tampa.  This list should be kept to an absolute minimum; please recognize that this superb AOC resource is quite limited.  To ease the strain on the AOC shop, we will work with each PI to ensure they arrive in Tampa with as much in hand as possible.

3.  Ferry flight/check flight procedures.  On occasion, AOC will perform an aircraft check flight, during which the instruments may be flown without power.  Aircraft maintenance needs may also dictate a ferry flight without science crew or SED techs on board.  Instruments should be designed with these eventualities in mind.  However, if your instrument requires standby power during this kind of flight, this may be provided at the discretion of AOC personnel.

If so, the flight crew will need to be briefed well ahead of time to ensure proper instrument operation.  Please provide with this document a bare-minimum checklist of instrument startup and shutdown procedures requested for these flights.

II.  Ground laboratory space

1.  Tampa space requests:

Power requirements:	60 Hz/ 1 A

Special requests:

2.  Field space requests:

Workspace, ft2:

Number of tables/chairs:

Power requirements:	60 Hz/1 A

Storage space, ft2:	12 sq ft

Other requests: