## Slide 1: A statistical downscaling procedure for improving multi-model ensemble probabilistic precipitation forecasts
Tom Hamill
ESRL Physical Sciences Division tom.hamill@noaa.gov
(303) 497-3060

## Slide 2: “National Blend of Models” project
Improve NWS National Digital Forecast Database (NDFD) fields using multi-model ensemble and multiple deterministic forecasts.
  Reduce need for forecaster manual intervention, free up forecasters for more decision support.
Eventually “Blend” will cover:
  all NDFD variables (e.g., Tmax, Tmin, T, Td, wind speed, direction, gust, sky cover, precip amount, snow amount, wave heighty) on 2.5-km grid.
  all US regions (CONUS, AK, HI, PR, Guam)
PSD’s role: improve multi-model precipitation, and more specifically here, POP. Asked to focus on 3-8 day period initially.

## Slide 3: NDFD POP product example

## Slide 4: Challenge: for NWS “National Blend” project, little training data exists, or it’s hard to get(and archive).
GEFS: will change soon to new version, obviating the existing reforecasts.
ECMWF: ~20-year, 1x weekly reforecasts, but have not been made available to us (yet).
CMC: ~ 5 years of reforecasts based on ERA-Interim with near-surface adjustment; not available for this project (yet).
No reforecasts for control/deterministic of various centers.
This limits the range of post-processing methodologies we feel comfortable trying.

## Slide 5: What might we reasonably do to post-process multi-model ensemble guidance?
Previously (Hamill, July 2012 MWR) multi-model ensembles for POP (July-Oct 2010) averaged to 1 degree grid verified against 1-degree CCPA.
This procedure produced reliable POP forecasts.
Models were ECMWF, UK Met Office, CMC, and NCEP.
1-degree forecasts are not high-enough resolution for Nat’l Blend; desire on 2.5-km grid.
Multi-model reliability, Day +5, > 1 mm

## Slide 6
Problem 1: coherent climatological detail, esp. in western US
at scales < 10 km, below the model-resolvable scales.
Why we don’t expect >10-km global ensemble forecasts to be reliable when verified against < 10-km analyses.

## Slide 7: Problem 2: sub-grid variability
precip
amount
east-west grid box #
large scale
1
2
3
4
5
Here we have a precipitation forecast along a segment of a latitude circle.

## Slide 8: Problem 2: sub-grid variability
precip
amount
east-west grid box #
large scale
1
2
3
4
5
fine scale
Here’s one possible fine-scale analysis that is consistent with the large scale.

## Slide 9: Problem 2: sub-grid variability
precip
amount
east-west grid box #
large scale
1
2
3
4
5
fine scale
But here’s yet another. There are infinitely many fine-scale vectors that
will spatially average to the correct large-scale vector.
So, when simulating a high-resolution ensemble, one should account
for sub-gridscale variability in a realistic manner.

## Slide 10: Proposed downscaling methodology
1 model
grid point
Precipitation amount
Ensemble member’s
forecast
Consider coarse resolution ensemble member forecast at a given grid point.
Repeat this process for every member at every grid point:

## Slide 11: Proposed downscaling methodology
1 model
grid point
Precipitation amount
Ensemble member’s
forecast
1 model
grid point
Precipitation amount
Matching coarse-
resolution
precip. analysis
Consider coarse resolution ensemble member forecast at a given grid point.
Find a past coarse-resolution analysis close in value to this forecast.
Repeat this process for every member at every grid point:

## Slide 12: Proposed downscaling methodology
1 model
grid point
Precipitation amount
Ensemble member’s
forecast
1 model
grid point
Precipitation amount
Matching coarse-
and fine-resolution
precip. analyses
Consider coarse resolution ensemble member forecast at a given grid point.
Find a past coarse-resolution analysis close in value to this forecast.
Extract the fine-resolution analysis at the same day and location.
Repeat this process for every member at every grid point:

## Slide 13: Proposed downscaling methodology
1 model
grid point
Precipitation amount
Ensemble member’s
forecast
1 model
grid point
Precipitation amount
Matching coarse-
and fine-resolution
precip. analyses
Consider coarse resolution ensemble member forecast at a given grid point.
Find a past coarse-resolution analysis close in value to this forecast.
Extract the fine-resolution analysis at the same day and location.
Define the downscaling vector.
Repeat this process for every member at every grid point:

## Slide 14: Proposed downscaling methodology
1 model
grid point
Precipitation amount
Ensemble member’s
forecast
1 model
grid point
Precipitation amount
Matching coarse-
and fine-resolution
precip. analyses
1 model
grid point
Precipitation amount
Downscaling vector
+ coarse-resolution
forecast.
Consider coarse resolution ensemble member forecast at a given grid point.
Find a past coarse-resolution analysis close in value to this forecast.
Extract the fine-resolution analysis at the same day and location.
Define the downscaling vector.
Add vector to the coarse-res. forecast to define the downscaled forecast.
Repeat this process for every member at every grid point:

## Slide 15: A different problem: systematic biases such as over-forecasting of drizzle.
Some regions,
such as in N
Nevada, models
tend to produce
precipitation
unrealistically,
day after day.
Such systematic
errors may
affect POP
reliability.

## Slide 16: CDF-based bias correction
A challenge is that if the CDFs are generated from small samples (with CDFs computed
separately for each grid point) may be noisy if computed using a small training sample size.

## Slide 17: Potential remedy for small sample size: use supplemental data locations
Idea is to supplement
training data at
each grid point using
n extra grid points
that have similar
observed climatology
and similar
forecast-observed
relationships, as
determined from
GEFS reforecasts.
In this plot, big symbol
is where we’re training,
smaller symbol where
we’re supplementing
training data.

## Slide 18: Smoothing the POP forecasts
Savitzky-Golay (S-G) filter used. For more details, see:
  http://research.microsoft.com/en-us/um/people/jckrumm/SavGol/SavGol.htm
  http://www.wire.tu-bs.de/OLDWEB/mameyer/cmr/savgol.pdf (good tutorial)
  Numerical Recipes text.
I coded up the S-G filter with a window size of 9 and using 3rd-order polynomial fitting.

## Slide 19: Savitzky-Golay filter
designed to preserve amplitudes, unlike more common nxn block smoothers
from Press et al. Numerical Recipes text

## Slide 20: Multi-model POP with statistical downscaling (but w/o Savitzky-Golay)

## Slide 21: Multi-model POP with statistical downscaling (but WITH Savitzky-Golay)
In this implementation, more
smoothing is applied in less
varied terrain of eastern US than
in more varied terrain of western
US.

## Slide 22: Strategy for POP forecasting implemented here.
POPs via multi-model ensemble, but with two modifications:
  Adjust each member with a CDF-based bias correction.
  Apply statistical downscaling as described previously.
Data used in subsequent demo:
  108-120 h coarse res. precip. forecasts, ensembles and deterministic for Jan 2014 from ECMWF, NCEP GEFS, UK Met, CMC.
  CDF bias correction trained using Nov-Dec 2013 108-120 h forecasts
  Long time series of both hi-res. and coarse-res. CCPA precip. analyses (2002-2013) for statistical downscaling.
Technique:
(1) CDF bias correct the forecasts using the past 60 days of forecasts and observations.
(2) Statistically downscale each member.
  (3) Compute probability from ensemble relative frequency.
  (4) Apply Savitzky-Golay smoothing to mimimize noise from sampling error.

## Slide 23: POP Reliability and skill, before & after
The BSS numbers look
rather high, even for the
raw ensembles (next slide).
I think this is because:
no big “dropouts” this
month?
(b) forecasts were very
different than the long-term
climatology, so skill relative
to climatology was larger
(the month was abnormally
dry in many locations).

## Slide 24: Reliability and skill of raw ensembles
ECMWF
NCEP
CMC
UK Met Office
Over this sample, the
multi-model raw
ensemble skill wasn’t
better than that of
the best forecast,
from ECMWF.

## Slide 25: Case study

## Slide 30: Benefits of CDF correction may not generalize to higher precipitation amounts
Applying the same methodology
to > 10 mm 12 h-1 forecasts, we
see little improvement as a
result of statistical downscaling
or CDF-based bias corrections.
It’s likely that 60 days, even with
supplemental locations, is not
enough samples to properly
adjust > 10 mm forecasts
(reforecasts and/or other
post-processing approach
needed)

## Slide 31: Conclusion / next steps
It appears to be possible to add skill, improve reliability of multi-model ensemble POP with statistical downscaling and CDF bias correction.
Improvements to probabilities for higher event thresholds more marginal, probably because CDFs used in bias correction are noisy with small sample size at higher quantiles.
This method is being evaluated in real time by forecasters.
  Pending evaluation, will migrate this technology to downscale using 4-km Stage IV precip analyses.

## Slide 32: Supplementary slides

## Slide 33: Methodology for weighting smoothed vs. original ensemble probabilities.

## Slide 34: Terrain-height variations

## Slide 35: Weight applied adjusted ensemble probabilities
Weight applied to CDF bias-corrected and downscaled multi-model ensemble probabilities