I.  General information:

1.  Mission name:  SENEX 2013

2.  Instrument name: NOyO3

3.  What is measured: Nitrogen oxides (NO, NO2, and NOy), and O3

4.  Short description of measurement technique:

NO – ozone-induced chemiluminescence

NO2 – UV photolysis to NO; ozone-induced chemiluminescence

NOy – catalytic conversion to NO; ozone-induced chemiluminescence

O3 – nitric oxide-induced chemiluminescence

5. Contact information for all personnel going to the field with this instrument:

(for multiple investigators, please list the PI or primary contact person first)

| Name | Email | Office phone | Cell phone |
| --- | --- | --- | --- |
| 1. Tom Ryerson | Thomas.b.ryerson@noaa.gov | 303-497-7531 | 303-818-1672 |
| 2. Ilana Pollack | ilana.pollack@noaa.gov | 303-497-5826 | 303-253-2767 |
| 3. |  |  |  |
| 4. |  |  |  |
| 5. |  |  |  |
| 6. |  |  |  |

II.  Specific information:

1. Total installed weight:	744 lbs (not including seat)

(rack, gas cylinders, hoses, cabling, pumps, inlets, permeation tubes, etc.)

| Rack weight and balance info | Allowed | Actual |
| --- | --- | --- |
| Weight, lbs.: | 700 | 480 |
| Overturning moment, in-lbs.: | 19600 | 11589 |

NOTE: Please also provide weight-and-balance information for all installed equipment.  Templates for standard electronics racks are available for download here.  PIs with non-standard installations will need to provide relevant information in a similar format.

2.  Individual subassembly info (weights should sum to total listed above)

| Component name | Location name and flight station | Weight, lbs |
| --- | --- | --- |
| 1. C3X rack | Sta. C3X; FS 445 | 480 |
| 2. C3X aft assembly | C3X sidewall; FS 485 | 164 |
| 3. NOy inlets & window plate | C3X window; FS 486 | 17 |
| 4. NOy scroll pump | C3X aft floor; FS 502 | 83 |
| 5. |  |  |

3.  Component power consumption in Amps

Please provide an electrical power diagram in Appendix A

| Component name | Location name | 400 Hz 3Ø | 400 Hz 1Ø | 60 Hz | 28VDC | 28VDC WOW |
| --- | --- | --- | --- | --- | --- | --- |
| 1. pod control panel | C3X rack |  |  |  | 1.0 |  |
| 2. NOy monitor | C3X rack |  | 0.3 |  |  |  |
| 3. NOy computer | C3X rack |  | 1.2 |  |  |  |
| 4. O3 generator | C3X rack |  | 1.4 |  |  |  |
| 5. NOy/O3 detector | C3X rack |  | 1.0 |  |  |  |
| 6. O3 absorption cell | C3X rack |  | 1.2 |  |  |  |
| 7. data distribution | C3X rack |  | 0.5 |  |  |  |
| 8. Flow zone | C3X rack |  | 5.0 |  |  |  |
| 9. LED power supply | C3X rack |  | 5.0 |  |  |  |
| 10. LED photolysis system | C3X rack |  | 1.0 |  |  |  |
| 11. NO/NO2 detector | C3X rack |  | 1.0 |  |  |  |
| 12. UPS & MKS valve | C3X rack |  |  | 2.0 |  |  |
| 13. DC power supply | C3X rack |  | 5.5 |  |  |  |
| 14. NOy scroll pump | C3X aft floor | 10/phase |  |  |  |  |
|  | Totals: | 10/phase | 23.1 | 2.0 | 1.0 | (none) |
|  |  | 400 Hz 3Ø | 400 Hz 1Ø | 60 Hz | 28VDC | 28VDC WOW |

4.  Inlet and exhaust information:

Please provide an inlet/exhaust line diagram in Appendix B

| Inlet/exhaust name | Location name and flight station | Hole size through hull, inches |
| --- | --- | --- |
| 1. NOy inlet | C3X window; FS 486 | 3.75 |
| 2. NO and NO2 inlet | C3X window; FS 486 | 0.375 |
| 3. O3 inlet | C3X window; FS 486 | 0.375 |
| 5. containment dump | C3X window; FS 486 | 0.375 |
| 6. cal dump | C3X window; FS 486 | 0.375 |
| 7. NOy/O3 exhaust | LIPF; FS 780 | 0.375 |

5.  Source of flow (name and location of pump or venturi)

| Pump name | Location name and flight station |
| --- | --- |
| 1. NOy/O3 scroll | C3X aft floor.; FS 502 |
| 2. diaphragm | C3X aft assy.; FS 485 |
| 3. |  |

6.  Installed hazardous materials or equipment:

(only for items installed in the aircraft for use during flight)

A.  Lasers:	none

B.  RF transmitters:  none

C.  Radioactive materials:	none

D.  Compressed gases: (1 ft3 = 28.32 liters; cabin volume = 4260 ft3 = 1.21 x 105 liters)

| Cylinder number: | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| Gas description | Pure CO | Pure NO | Pure O2 | Pure air | NO cal |
| Mixing ratio | 100% | 100% | 100% | 100% | 1.5 ppm |
| Cylinder size (ft3) | 1.8 | 1.8 | 23 | 50 | 30 |
| Max pressure (psig) | 1000 | 500 | 2000 | 2200 | 2200 |
| # installed on aircraft | 1 | 1 | 1 | 1 | 1 |
| Location on aircraft | C3X aft | C3X aft | C3X aft | C3X aft | C3X aft |
| Service frequency | every 9 flights | every 9 flights | every 4 flights | every 3 flights | never |
| toxic/flammable gases: |  |  |  |  |  |
| In containment vessel? | Yes | Yes |  |  |  |
| Gas alarm provided? | Yes | Yes |  |  |  |
| MR if vented to cabin, ppmv | 420 | 210 |  |  |  |
| OSHA 8-hr PEL, ppmv | 35 | 25 |  |  |  |
| 30-min IDLH, ppmv | 1500 | n/a |  |  |  |

E.  Chemicals (solids and liquids):

| Chemical number: | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Name | Dry ice | Water | Water | N-150 catalyst |
| Concentration | 100% | 100% | 100% | 100% |
| Amount | 7 kg | 75 ml | 500 ml | 50 g |
| Container description | PMT housing | PFA volume | Photolytic converter | Pump exhaust trap |
| Purpose | Cooling | water addition | water cooling | Ozone scrubber |
| Solution pH | n/a | 5.5 | 5.5 | n/a |
| Spill kit provided? | no | no | no | no |

F.  Cryogens:  Dry ice (solid CO2)

Location:	C3X rack – two PMT housings

Description:    Dry ice (2 places)

Container description:  two PMT housings

Quantity on board per flight:  7.0 kg

Serviced on the aircraft?  yes

G.  UPS and battery installation:

TrippLite SmartPor 500RT-1U sealed lead-acid battery;

Battery disconnect accessible from the front panel

H.  Motors

Description:  NOy scroll pump

Motor current draw: 3Ø, 400Hz, 18A/phase startup, 9A/phase running

Thermal interlock enabled? Yes

Description:  NO2 photolysis: water circulation pump to LEDs

Motor current draw: 24 VDC, 7A max current

Thermal interlock enabled? No

Description: diaphragm pump

Motor current draw: 28 vDC, 2. 0 A startup, 1.0 A running

Thermal interlock enabled? No

I.  Operator seat requests -

Test flights:  1

Transit flights:  1

Science flights:  1

7.  Data and plumbing drops

Network (Cat. 5/6 ethernet) drops requested:  1

Serial drops requested: none

IRIG-B drops (BNC coax connector) requested:  none

Vacuum/exhaust/ emergency dump lines:

| Name | Flow rate, slpm | Line pressure, Torr | Pump type | Trace gas concentration(s) |
| --- | --- | --- | --- | --- |
| 1. scroll pump | 4 | Ambient | Dry scroll | 100 ppm O3, 10 ppm NO |
| 2. diaphragm pump | 0.4 | Ambient | Diaphragm | None |
| 3. |  |  |  |  |
| 4. |  |  |  |  |

Ground gas service lines (number, location, type of service):

Pure air – C3X to freefall chute, ¼” o.d., 40 psi

Pure oxygen – C3X to freefall chute, 1/8” o.d., 30 psi

Other gas lines (number, location, type of service):

NO cal – C3X to Sta. 5, 1/16” o.d., 40 psi

Will you be sending data to the AOC data station?  If so, please provide the following information:  no

8.  Aircraft access

- flight days:

Pre-flight time requested at aircraft (hours): 3 hours

Routine pre-flight ground support required? 	none

(stands, ladders, forklifts, covers, external equipment, etc.)

Routine post-flight time requested at aircraft (hours): 1 hour

Routine post-flight ground support required? none

(stands, ladders, forklifts, covers, external equipment, etc.)

b.  non-flight days:

Routine external access to inlets or zenith mounts required?  no

(please describe location, how often, for how long, type of ground support equipment needed, weather constraints, etc.)

Please note there is zero access and zero power to the aircraft (including pods) on hard-down days.  These occur at least once every seven calendar days while in the field.

9.  Aircraft maneuvers

Briefly describe in-flight calibration frequency, duration, altitudes desired:

none

Briefly describe instrument sensitivity to flight conditions:

(issues during roll/pitch, ascent/descent, sampling in cloud, icing etc.)

NOy artifacts in precipitation, at NH3 > 10 ppb, and NH4NO3 > 5 µg/m3

10.  Miscellaneous

1.  Hazmat for preflight/postflight calibrations:  Please describe fully any additional hazardous materials - compressed gases, solvents, radioactive ion sources – that you anticipate temporarily bringing onto the aircraft for periodic instrument calibration purposes  (e.g., n-butanol in a CN counter, 210Po in a DMA, a UPS for power, compressed gas cylinders for calibrations, etc.)

none

2.  Fabrication and sheet metal support:  Please describe fully any anticipated requests for fabrication or sheet-metal support during installation in Tampa.  This list should be kept to an absolute minimum; please recognize that this superb AOC resource is quite limited.  To ease the strain on the AOC shop, we will work with each PI to ensure they arrive in Tampa with as much in hand as possible.

none

3.  Ferry flight/check flight procedures.  On occasion, AOC will perform an aircraft check flight, during which the instruments may be flown without power.  Aircraft maintenance needs may also dictate a ferry flight without science crew or SED techs on board.  Instruments should be designed with these eventualities in mind.  However, if your instrument requires standby power during this kind of flight, this may be provided at the discretion of AOC personnel.

If so, the flight crew will need to be briefed well ahead of time to ensure proper instrument operation.  Please provide with this document a bare-minimum checklist of instrument startup and shutdown procedures requested for these flights.

none

II.  Ground laboratory space

1.  Tampa space requests:  the usual

Power requirements:

Special requests:

2.  Field space requests:

Work space, ft2:  	100 ft2

Number of tables/chairs:  2 tables, 2 chairs

Power requirements:  	10 A at 110vAC

Storage space, ft2: 	150 ft2

Other requests:	none