Aerosol Impactor Box – Wiring Diagram

P1 = Amp, MateNLok, 2x3 shells w/ sockets (connector to electronic ball valve)

P2 & P3 = Amp, MateNLok, 1x3 shell w/ pins (connectors to solenoids)

P4 = MateNLok 3x3 shell w/ pins (front panel of impactor box)

(G) = Ground

(H) = Hot (=L, Line on some connectors)

(N) = Neutral

Wire color and gauge is expressed like G-18 (green, 18 AWG)

Switched A/C power – connections to front panel connector

Vaisala Panel Mount Pin-out

Pin	Parameter

1	RH

2	Temp

3	7-28 VDC

4	common

Vaisala Humitter Sensor  Pin-out

Wire	Parameter

BRN	RH

V	Temp

Y	7-28 VDC

G	common

# Text boxes

P4-1

P2-1

P4-2

P4-3

P2-2

P2-3

N.O. Valve

P3-1

P3-2

P3-3

N.C.

Valve

(G) G-18

(H) B-18

(N) W-18

IEC

B-18

W-18

G-18

(L)

(N)

(G)

P4-5

P4-6

N/C

BRW-18

R-18

P1-1

P1-2

P1-3

P1-4

P1-5

P1-6

N

H

G

To switched a/c for solenoid valves

G

To switched a/c for ball valve