Precision Infrared Radiometer (PIR) data from the 1995 UV-B Spectroradiometer 
Intercomparison held at the Table Mountain Test Facility Boulder, Colorado 
June 14-23, 1995.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as PIR###.TXT, where ### refers to the Julian date, contain 
the ancillary data from the PIR's for the days that solar spectral scans were 
taken during the intercomparison.  The data in the files is in raw form as 
logged from the instrument in mV.  The calibration factors to be applied to 
the data are listed below.

The description of the data files is as follows;

Year, Julian date, HourHourMinuteMinute (GMT), PIR (serial # 29143), 
PIR (serial # 29144), PIR (serial # 29149), the next six columns are the 
respective case and dome resistances and then the next nine columns are 
the respective standard deviations of the three PIR's, 3 case, and 3 dome 
temperatures.

The calibration factors to be used with the data listed in mV are,

PIR Serial Number        Calibration Factor (x 10E-6 V/(W/mE2))

                                                          SRRB

                                                          C1
29143                                                 3.62
29144                                                 3.65
29149                                                 3.86

The C2 constants to be used in the formula are given as follows;
(These are dimensionless constants)

                                                           C2 (dome)
29143                                                 2.85
29144                                                 2.65
29149                                                 2.36


Data manipulation equations listed below:


Calculate:
                    Case temperature                    T (case) (K)
                    Dome temperature                  T (dome) (K)

T (c/d) = 10E5/(273.09+26.3198*L+0.278237*LE2+0.0196739*LE3)

where            L = ln((R (c/d))/1000)   and R (c/d) is in Ohms


                      R (case)  Case Resistance (Ohms)
                      R (dome) Dome Resistance (Ohms)

IRRADIANCE;

I(W/mE2)= V/(1000*C1) +SIGMA*T(case)E4 + C2*SIGMA*
(T(case)E4-T(dome)E4)


where  
              V                              is in (mV)
              T(case or dome)        is in (K)
              C1                            is in (V/(W/mE2)
              SIGMA                    is in (W/(mE2*KE2)  Stephan-Boltzman 
                                               constant 5.67E10-8 (W/(mE2*KE4)