Precision Solar Pyranometer data from the 1995 UV-B Spectroradiometer 
Intercomparison held at the Table Mountain Test Facility Boulder, 
Colorado June 14-23, 1995.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_95/psp
directory.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as PSP###.TXT, where ### refers to the Julian date, contain 
the ancillary data from the PSP's for the days that solar spectral scans were 
taken during the intercomparison.  The data in the files is in raw form as 
logged from the instrument in mV.  The calibration factors to be applied to 
the data are listed below.

The description of the data files is as follows;

Year, Julian date, HourHourMinuteMinute (GMT), Downwelling PSP 
(serial # 29613), Shaded PSP (serial # 29614), Upwelling PSP 
(serial # 29616), the next three columns are the respective standard 
deviations of the three PSP's.

The calibration factors are to be used for the data files listed in mV,

Convert the data in mVolts to Volts by multiplying (1/1000)V/mV
first before applying the calibration factors.

PSP Serial Number   Calibration Factor (x 10E-6 V/(WmE-2))

29613                                                 8.528
29614                                                 8.306
29616                                                 8.460