Solar Light Model 501 UV-Biometer data from the 1995 UV-B
Spectroradiometer Intercomparison held at the Table Mountain 
Test Facility Boulder, Colorado June 14-23, 1995.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_95/solar
directory.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

In the solar directory there are three types of files.  Files listed as
SOL###.TXT, where ### refers to the Julian date, are the raw data files.
The files contain data as such;
Line out from logger, Year, Julian date, HourHourMinuteMinute (GMT),
Solar Light 501 (serial #1886) ( in mV), bad data, Solar Light 501 
(serial #1898) ( in mV), the next three columns are the respective 
temperature signals in mV, disregarding the middle one, and the next 
six columns are the standard deviations, disregarding the second and 
the fifth column which are associated with the bad data

The files listed as SOLAR###.TXT
contain the UV broadband data from the Solar Light's for the days
that solar spectral scans were taken during the intercomparison.

The data in the files has had the calibration factor applied to convert the
raw voltages to MED/Hour units.  The conversion factor to change from
MED/Hr's to Diffey Weighted Irradiance is listed below and in the file.

The files listed as SOLAR###.XLS contain the same data as the 
SOLAR###.TXT files, but are saved in EXCEL 5.0c format.  Conversion
factors have been applied and a plot of the MED/Hr versus Time is shown.
When using ftp these files must be transferred in binary mode.

Conversion factors used for the Solar Light 501 Radiometers:


(1/1000)V/mV*(data(mV))*4.0 (MED/Hour)/Volt, to convert
from mV to MED/Hour units.

Use the conversion factor, 0.0583 (W/mE2)/(MED/Hour) to convert
from MED/Hour units to (W/mE2)-Diffey Weighted Irradiance.

Temperature conversion:  T(degrees Celsius) = (50)*(1/1000(V/mV))*data-25